## Slide 1: Digital Zoom
By Ido W. and Dvir H.
May, 2025

## Slide 2: System Overview
Goals:
digital zoom on FPGA:
Operates OV7670 camera as input and VGA monitor for display.
Implement zoom x 2.
Solve zoom pixelation by Bilinear Interpolation.

## Slide 3: Project’s steps
Architecture – Key FPGA Modules.
Code implementation (RTL)
Simulations
Synthesis
Place & Route - .xdc

## Slide 4: Architecture – Key FPGA Modules.
Initial architecture:
Capture → BRAM → VGA
Capture → Zoom → BRAM / 4 → VGA

## Slide 5: Architecture – Key FPGA Modules.
Final architecture:
Capture → Zoom → BRAM2 → Bili → BRAM1 → VGA
Capture → Zoom → BRAM2 → VGA
Capture → BRAM1 → VGA

## Slide 6: Flow – block diagram
Pixel data, clk, sync signals
SCCB Config, clk, reset
Sync signals, pixels

## Slide 7: Main State Machine
Idle – No VGA
Active VGA -
Rainbow screen
Camera Display 640×480
Camera tuning setup
reset
Camera cntl
config
Zoom x 2
Cropped
320x240
zoom
Zoom x 2
filtered
640x480
Bili cntl

## Slide 8: Module: Controller
Config, clk, reset
Configure registers with protocol SccB (I2C like), 97.65KHz
B"01000010" = x"42"
B“1000_0000" = x“80"

## Slide 9: Module: Capture
Collects pixel data by sampling two consecutive 8-bit values to form one pixel.
Converts camera data from RGB565 to RGB444 (to match the board’s VGA pin format).
Writes the pixel data to BRAM.
Zoom mode – stores only the center portion of the image pixels in BRAM.
Pixels data, clk, sync signals
Capture → BRAM → [VGA]

## Slide 10: Module: BRAM
Collects pixel data by sampling two consecutive 8-bit values to form one pixel.
Converts camera data from RGB565 to RGB444 (to match the board’s VGA pin format).
Writes the pixel data to BRAM.
Zoom mode – stores only the center portion of the image pixels in BRAM. (Use only ¼ BRAM)
  Storge size:
  Width 12 bits (= 1 pixel)
  Depth 307,200 (= 640x480)
Capture → BRAM → [VGA]

## Slide 11: Module: BRAM
Collects pixel data by sampling two consecutive 8-bit values to form one pixel.
Converts camera data from RGB565 to RGB444 (to match the board’s VGA pin format).
Writes the pixel data to BRAM.
Zoom mode – stores only the center portion of the image pixels in BRAM. (Use only ¼ BRAM)
  Storge size:
  Width 12 bits (= 1 pixel)
  Depth 307,200 (= 640x480)
Capture → BRAM → [VGA]

## Slide 12: Two Content Layout with Table
First bullet point here
Second bullet point here
Third bullet point here
Class | Group 1 | Group 2
Class 1 | 82 | 95
Class 2 | 76 | 88
Class 3 | 84 | 90

## Slide 13: Title and Content Layout with SmartArt
Step 1 Title
Step 2 Title
Task description
Task description
Task description
Task description
Task description
Task description
Task description
Step 3 Title
Task description
Task description
Step 4 Title
Task description
Task description

## Slide 14: Add a Slide Title - 1

## Slide 15: Add a Slide Title - 2

## Slide 16: Add a Slide Title - 3

## Slide 18: Add a Slide Title - 4

## Slide 19: Add a Slide Title - 5